## Slide 1
  COURSE:
  Embedded System Design And Iot
  COURSE CODE:25EC2206
  TOPIC:
  M1-8-A first program: blink an LED on a Nucleo-H743ZI board

## Slide 2: M1-8-A first program: blink an LED on a Nucleo-H743ZI board
Hardware Info
User LED (LD1) → PA5
LED is active via GPIO output
CubeMX Configuration
In the .ioc file:
Set PA5 → GPIO_Output
No pull-up/pull-down
Keep default clock settings
Generate code

## Slide 3: Program 1.LED Blink Program (main.c)
Write only inside USER CODE section:
/* USER CODE BEGIN WHILE */ while (1) { HAL_GPIO_WritePin(GPIOA, GPIO_PIN_5, GPIO_PIN_SET); // LED ON HAL_Delay(500); HAL_GPIO_WritePin(GPIOA, GPIO_PIN_5, GPIO_PIN_RESET); // LED OFF HAL_Delay(500); } /* USER CODE END WHILE */

## Slide 4: Program-2:Toggle Program
/* USER CODE BEGIN WHILE */ while (1) { HAL_GPIO_TogglePin(GPIOA, GPIO_PIN_5); HAL_Delay(500); } /* USER CODE END WHILE */