## Slide 1
EMBEDDED SYSTEMS ARCHITECTURE
STM32H7 memory map
Flash, ITCM, DTCM, AXI SRAM, and the peripheral region
A closer look at where code and data live in the Cortex-M7 address space, and which bus gets you there

## Slide 2
Agenda
Topics covered in this presentation
01
Memory map overview
The address space at a glance, region by region
02
Flash memory
Code storage, the ART accelerator, and access latency
03
ITCM & DTCM
Tightly-coupled memory wired straight to the core
04
AXI SRAM
General-purpose RAM shared by CPU and DMA
05
Peripheral region
Memory-mapped registers and the AHB/APB bridge
06
Key takeaways
Matching each region to the right use case
2

## Slide 3
Memory map overview
Five regions, each reached over a different bus path. The choice of region is a choice about speed, sharing, and access pattern.
Two access paths
ITCM/DTCM bypass the AXI matrix; everything else routes through it.
Speed vs. sharing
Tightly-coupled memory is fastest, but isolated from DMA.
One common ground
AXI SRAM is reachable by both the CPU and DMA controllers.
Flash memory
0x0800 0000 - 0x081F FFFF
code storage, up to 2 MB
AXI SRAM (D1 domain)
0x2400 0000 onward, ~512 KB
shared CPU + DMA RAM
Peripheral region
0x4000 0000 - 0x5FFF FFFF
GPIO, USART, timers, RCC
DTCM
0x2000 0000 - 0x2001 FFFF, 128 KB
core data bus, 0 wait-state
ITCM
0x0000 0000 - 0x0000 FFFF, 64 KB
core instruction bus, 0 wait-state
high addr.
low addr.
3

## Slide 4
Flash memory
0x0800 0000 - 0x081F FFFF · up to 2 MB, dual-bank
What lives here: Compiled program code and constant data; execution starts here after reset.
Bus path: Reached over the AXI bus through the embedded flash controller.
Latency: Flash cells are slower than SRAM, so reads need wait states at higher clocks.
Caching: An ART accelerator and instruction cache sit in front of flash to hide that latency.
Practical tip: Hot loops are often copied into ITCM or SRAM at startup to avoid wait states.
Flash array
2 MB
ART + I-cache
hides latency
AXI bus
interconnect
Cortex-M7 core
fetches code
4

## Slide 5
ITCM and DTCM
ITCM 0x0000 0000-0x0000 FFFF · DTCM 0x2000 0000-0x2001 FFFF
Direct core connection: Wired straight to the Cortex-M7's dedicated buses, bypassing the AXI matrix entirely.
ITCM: Holds instructions on the instruction bus, ideal for interrupt handlers and hot code paths.
DTCM: Holds data on the data bus, best for stacks and buffers needing deterministic timing.
Performance: Zero wait-state, full core-speed access; the fastest memory on the chip.
The gotcha: DMA controllers cannot efficiently reach DTCM since it sits off the AXI matrix.
Cortex-M7
core
ITCM
instruction bus
DTCM
data bus
DMA controller
no efficient path
5

## Slide 6
AXI SRAM (D1 domain)
0x2400 0000 onward · ~512 KB, plus SRAM1-4 elsewhere
General-purpose RAM: Sits on the main AXI crossbar rather than a dedicated core bus.
Shared access: Reachable by the Cortex-M7 core and by DMA controllers and other bus masters.
Common use: The natural home for buffers shared between peripherals and application code.
Trade-off: More flexible than TCM, but contends with other bus masters at AXI bus speed.
Beyond D1: Additional SRAM1-4 blocks exist in other power domains for specialised sharing.
AXI SRAM
512 KB shared
AXI crossbar
Core
DMA1
DMA2
multiple bus masters reach the same RAM
6

## Slide 7
Peripheral region
0x4000 0000 - 0x5FFF FFFF
What lives here: Memory-mapped registers for every on-chip peripheral: GPIO, USART, SPI, timers, RCC.
Bus path: Reached over AHB and APB buses, which bridge into the main AXI matrix.
Access rules: Marked non-cacheable and strictly-ordered by default in the MPU configuration.
Why it matters: Registers must reflect real hardware state immediately, never a stale cached value.
Practical effect: Reads and writes always hit the hardware directly, never a cache line.
AXI matrix
AHB / APB bridge
GPIO
USART
SPI
Timers
RCC
registers, accessed directly - no caching
7

## Slide 8
Key takeaways
1
ITCM and DTCM are wired directly to the Cortex-M7 core, giving zero wait-state access at the cost of isolation from DMA.
2
AXI SRAM is the common ground: the only region reachable by both the CPU and DMA controllers efficiently.
3
Flash holds code but is the slowest region, so the ART accelerator and instruction cache mask its latency.
4
The peripheral region is intentionally non-cacheable, so register reads always reflect real hardware state.
5
Matching data and code to the right region is a deliberate trade-off between speed, sharing, and determinism.
ARM Cortex-M7 + STM32H7 series